EURO FuelSaver S.r.l. SUPER TECH®

+ energy        + economy        + ecology

www.supertech.it

The present Refer Book doesn't contain the integral version
of the documents but only a summary describing the obtained results.
Whoever would wish to receive the integral version,

shall send a request to the General Management.

Sede Operativa: Via Siracusa, 34 – 90141 Palermo - tel +39 091 308999

Direzione Commerciale: Viale Virgilio, 58/C-1° p. – 41100 Modena-Italia tel.: +39 059 897215 fax +39 059 897216

Sito Internet: www.supertech.it - e.mail: eurofuel@neomedia.it D.G. paolosalemi@libero.it

P.IVA 05558901004 - Capitale sociale interamente versato € 102.328

| Date | Institute/Company | Test | Results | Attached |
| --- | --- | --- | --- | --- |
|  |  | Labor. | Road | Gas emis reduction | Consump Reduc | Documentation |
| 04/01/07 | LATVIA | x |  |  | 13% |  |

Conclusion of experiments with equipment of Super Tech

- Objective of experiments: prescribe influence of Super Tech equipment to Otto engine for fuel consumption and reduction of gas emission.

- Place and time of experiments:

Scientific Laboratory of alternative fuels, November 2007,

2 P. Lejina, Jelgava, LV-3001

3.   Object of experiments:

Car Audi A4, 1,8 litres Otto engine, year 1995

4.   Schedule of test

  - Power test;

  - IM – 240 cycle;

  - Regime with fixed speed 50 km/h;

  - Regime with fixed speed 90 km/h.

- Results of experiments:

  - Application of fuel in combined “city-outside the city” cycle IM-240 (240 seconds, ~3,1 km) without equipment of Super Tech 237,64 grams, with equipment of Super Tech 223,82 grams. Average fuel consumption with SuperTech – 5,8%.

  - Fuel consumption with fixed speed (50 km/h) without SuperTech – 6,44 l/100km, with SuperTech – 5,76 l/100km. Average fuel saving ~ 11%. Fuel saving in 100 km run – 0,68 litres.

  - Fuel consumption with fixed speed (90 km/h) without SuperTech – 5,81 l/100km, with SuperTech – 5,07 l/100km. Average fuel saving ~ 13%. Fuel saving in 100 km run – 0,74 litres.

  - Fundamental increase of power not acquired. In separate range of engines RPM have acquire power increase till 3%.

Responsible persons for test performance:

Asist. Mg.sc.ing.                                                Vilnis Pirs

Asist. Mg.sc.ing.                                                 Zanis Jesko

Asist. Bc.sc.ing.                                                   Janis Laceklis-Bertmanis

Director of Motor Vehicle Institute                    Dainis Berjoza

Assoc.prof., Dr.sc.ing.

/ 2007.04.January - mistake / it means 2008.04 of January

# Text boxes

REFER BOOK

Latvia

Reference

# LATVIA